## Slide 1: Welcome to the Webinar Offered by: National Microelectronics Security Training (MEST) Center
Sponsors:
Notes: Welcome to the Microelectronics…webinar titled this this
Until 12:03 or send to instructor to have them keep slide for the first 5-8 minutes MEST Logo title and logo name
Uf logo and OSU logo, sponsors AFRL and Nimbis.

## Slide 2: Introduction to System on Chip Development of a Basic System-on-Chip Architecture in FPGA
Abigail Butka, Kawser Ahmed Muhammed, Christophe Bobda
National Micro Electronics Security Training (MEST) Center

## Slide 3: Agenda
Introduction and Motivation
System on Chip
  Introduction and Motivation
  Definition
  Examples
  Benefits
  Challenges
Basic Lab Architecture
Conclusion and Discussion
National Micro Electronics Security Training (MEST) Center

## Slide 4: Introduction and Motivation - Moore’s law
The most important trend in computer systems
Predicted in 1965 by Intel co-founder Gordon Moore
IC transistor capacity has doubled roughly every 18 months for the past several decades
Today’s high-end chips may contain Billions transistors
  Transistor gate lengths (feature size) are now in term of nanometers
  From 180nm in the 2000s to 40nm in 2014 and 3nm today
  In 2020, Samsung and TSMC entered volume production of 5 nm chips, manufactured for companies including Apple, Marvell, Huawei and Qualcomm
  Approximately every 18 months the number of transistors on a chip doubles – Moore’s law
The Consequences
  Components formerly connected on a Printed Circuit Board can now be integrated onto a single chip
  Hence the development of System-On-Chip
National Micro Electronics Security Training (MEST) Center

## Slide 5: SoC- Definition
System: A collection of all kinds of components and/or subsystems that are appropriately interconnected to perform the specified functions for end users.
System-on-Chip (SoC): Complete system on a single chip?
SoC not only chip, but more on “system”
SoC = Chip + Software + Integration
National Micro Electronics Security Training (MEST) Center

## Slide 6: SoC- Definition
The SoC Hardware includes
  Embedded processor
  Hardware IPs
  Peripherals and analog circuitry
  Embedded memory
  Interconnect
The SoC Software includes:
  OS, compiler, simulator, firmware, driver, protocol stack, Integrated development environment (debugger, linker), Application interface (C/C++, assembly)
A key benefit of SoCs is the concept of IP Reuse
  IP reuse allows hardware designers to reduce development time by not re-making the wheel
National Micro Electronics Security Training (MEST) Center

## Slide 7: SoC- Examples
Apple A14 Bionic
National Micro Electronics Security Training (MEST) Center

## Slide 8: SoC- Benefits
Reduced size
Reduced overall system cost
Lower power consumption
Increased performance
Increased functionality/performance in reduced footprint
Simplified PCB design
Increased product mechanical robustness
And more and more advantages …
National Micro Electronics Security Training (MEST) Center

## Slide 9: SoC- Challenges
Increasing complexity
  Hardware/Software integration!
  Time-to-market pressure
    Shorter product lifespan
    Shorter design cycles
  Verification bottleneck
    Assume you must 100% verify a two-input 32’bit multiplier. This is 2^64 = 18,446,744,073,709,551,616 test cases!!
    If it takes 1ns to perform one test, fully testing this simple multiplier would take over 500,000 years
National Micro Electronics Security Training (MEST) Center

## Slide 10: SoC- Application Challenges
Speech Signal Processing
Image and Video Signal Processing
Information Technologies
  PC interface (USB, PCI,PCI-Express, IDE,..etc) Computer peripheries (printer control, LCD monitor controller, DVD controller,.etc) .
Data Communication
  Wireline Communication: xDSL, Gigabit Ethernet, Etc…
  Wireless communication: BlueTooth, WLAN, 2G/3G/4G, WiMax, UWB, etc…
Consumer
  Game box
  Digital Camera
Automotive
National Micro Electronics Security Training (MEST) Center

## Slide 11: Case Study and Tutorial