## Slide 1: Welcome to the Webinar Offered by: National Microelectronics Security Training (MEST) Center
Sponsors:
Notes: Welcome to the Microelectronics…webinar titled this this
Until 12:03 or send to instructor to have them keep slide for the first 5-8 minutes MEST Logo title and logo name
Uf logo and OSU logo, sponsors AFRL and Nimbis.

## Slide 2: Introduction to PetaLinux Embedded Operating Systems
Abigail Butka, Kawser Ahmed Muhammed, Wade Fortney, Christophe Bobda
National Micro Electronics Security Training (MEST) Center

## Slide 3: Agenda
System-on-Chip Refresher
Operating Systems
  Definition
  Uses
  Benefits
  Application to Systems-on-Chip
Basic Lab Architecture
Conclusion and Discussion
National Micro Electronics Security Training (MEST) Center

## Slide 4: SoC- Architecture
National Micro Electronics Security Training (MEST) Center
Processor
Program
memory
…
HA Interface
Bus
IP1
Software
Tasks
Peripheral
Peripheral
SW Interface
IP2
IP3

## Slide 5: Operating Systems

## Slide 6: What is an Operating System?
When you think of an operating system, what do you think of?
National Micro Electronics Security Training (MEST) Center

## Slide 7: What is an Operating System?
An operating system is a layer of software that acts as an intermediary between the computer hardware and software applications
Operating systems allow users to utilize hardware, like your computer’s CPU, without requiring knowledge of how the hardware works
Two main views to characterize operating systems
  Service Provider
  Resource Manager
National Micro Electronics Security Training (MEST) Center

## Slide 8: Operating System as a Service Provider
As a service provider, the operating system hides the low-level details from the user to provide a simplified experience
Task
  Application Programming Interfaces (APIs) to allow applications to request resources
  User Interface or Graphical User Interface
  File-system management
Advantage
  Performance
  Modularity
  Memory usage
  Time to market
  Reliability
  Maintainability
  Portability
  Scalability
National Micro Electronics Security Training (MEST) Center

## Slide 9: Operating System as a Resource Manager
As a resource manager, the operating system ensures that each program gets its required time with and space on their required resources
Task
  Provide the environment under which program can run
  Control and manage the access to resources by concurrent programs
  Processor management
  Memory management
  Provide protection and security
National Micro Electronics Security Training (MEST) Center
Application 1
Application 2
Resource Management
Application n
Resources (Hardware)

## Slide 10: Operating System Concepts
The operating system is a layer of software that acts as an intermediary between the computer hardware and software applications. It provides:
Process management
  Processes need resources to accomplish their task
  Upon completion, resources must be re-allocated
  Can be single-threaded (sequential instructions) or multi-threaded (multiple instructions running at once)
Memory management
  Ensure all data/instructions are in memory before process execution
  Determine what is where inside of the memory and when
  Allocating and deallocating memory
Operating system is responsible for:
  Creating and deleting user and system processes
  Suspending and resuming processes
  Providing mechanisms for process synchronization, communication, and deadlock handling
  File-system management
  Etc...
National Micro Electronics Security Training (MEST) Center

## Slide 11: Operating System Concepts
Additionally, the operating system must provide protection and security
Protection – any mechanism for controlling access of processes or users to resources defined by the OS
Security – defense of the system against internal and external attacks
Systems generally first distinguish among users to determine who can do what
User identities (user IDs, security IDs) include name and associated number, one per user
User ID then associated with all files and processes of that user to determine access control
National Micro Electronics Security Training (MEST) Center

## Slide 12: Why Should we use Operating Systems?
Operating systems provide many useful functions such as:
  User interface, Graphics User Interface (GUI), and Command Line Interface
  Program execution
  I/O operations
  File-system manipulation
  Error detection
  Hardware resource management, mapping, and allocation
National Micro Electronics Security Training (MEST) Center

## Slide 13: How do we use Operating Systems in SoCs?
PetaLinux
  PetaLinux is a set of tools that can create a specialized, embedded Linux environment for Xilinx FPGAs
  This Linux environment, or operating system, is commonly referred to as PetaLinux
  The PetaLinux tools provide a workflow for creating, building, and deploying Linux
  This operating system is unique because it is designed to work with FPGAs and the Vivado workflow
    PetaLinux can import System-on-Chip .xsa designs
    This allows the user to access and modulate GPIO pins or custom hardware from the operating system
    Provides a high abstraction method of accessing low-level components
PetaLinux creates an operating system similar to other Linux-based operating systems, only it can interface directly with Xilinx’s hardware
National Micro Electronics Security Training (MEST) Center

## Slide 14: Case Study and Tutorial